本文档下载自文档下载网，内容可能不完整，您可以点击以下网址继续阅读或下载：

http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html

汽车ECE_R10.04标准

汽车行业的ECE标准

Original English version

Acknowledgement:

The following consolidated text of the Regulation was edited by Daimler AG.

To integrate amendments, corrigenda etc. the legal documents available online at http://www.unece.org were used.

AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNI-TION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (*)

UNIFORM PROVISIONS CONCERNING THE APPROVAL OF VEHICLES

WITH REGARD TO ELECTROMAGNETIC COMPATIBILITY

The following text contains two different amendment markings:

The red marginal line marks the amendments as per the last official amendment instruction. Red text within such officially amended sections marks the actual new/amended wording http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlas identified by the ALO team.

Revisions, Amendments and Supplements E/ECE/324-E/ECE/TRANS/505/.../Add.9

E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.1 E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.2

E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.2/Amend.1 E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.2/Amend.1 E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.2/Corr.1 E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.2/Amend.2 E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.3

E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.3/Corr.1 E/ECE/324-E/ECE/TRANS/505/.../Add.9/Rev.3/Amend.1 E/ECE/324-E/ECE/TRANS/505/.../Add.9/… E/ECE/324-…

Original version Amend. 01 Amend. 02

Amend. 02, Corr. 1 Amend. 02, Suppl.1 Amend. 02, Corr. 2 Amend. 02, Suppl.2 Amend. 03

Amend. 03, Corr. 1 Amend. 03, Suppl. 1

Amend. 04 [pursuant to doc. WP.29/2011/8   para. 53 of the report]

Amend. 04, Corr. 1 [pursuant to doc. WP.http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html29/2011/83]

In force: 01.04.1969 In force: 19.03.1978 In force: 03.09.1997 In force: 11.03.1998 In force: 04.02.1999 In force: 10.11.1999 In force: 12.08.2004 In force: 11.07.2008 In force: 10.03.2010 In force: 09.12.2010 In force: 28.10.2011 In force: 28.10.2011

(*)

Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

UNIFORM PROVISIONS CONCERNING THE APPROVAL OF VEHICLES

WITH REGARD TO ELECTROMAGNETIC COMPATIBILITY

Regulation

1. Scope............................................................................................................................4 2. Definitions.......................................................................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html..............................4 3. Application for approval..................................................................................................6 4. Approval........................................................................................................................8 5. Markings........................................................................................................................9 6. Specifications in configurations other than "RESS charging mode coupled to   the power grid".............................................................................................................10 7. Additional specifications in the configuration "RESS charging mode coupled to   the power grid".............................................................................................................15 8. Amendment or extension of a vehicle type approval following electrical/  electronic sub-assemblhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmly (ESA) addition or substitution..................................................21 9. Conformity of production..............................................................................................21 10. Penalties for non-conformity of production.....................................................................22 11. Production definitely discontinued.................................................................................22 12. Modification and extension of type approval of a vehicle or ESA.....................................22 13. Transitional provisions.................................................................................................23 14. Names and addresses of Technical Services conducting approval tests and of

Administrative Departments..........................................................................................23 Appendix 1  List of standards referred to in this http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlRegulation.......................................................24 Appendix 2  Vehicle broadband reference limits (Antenna-vehicle separation: 10 m)..................26 Appendix 3  Vehicle broadband reference limits (Antenna-vehicle separation: 3 m)....................27 Appendix 4  Vehicle narrowband reference limits (Antenna-vehicle separation: 10 m)................28 Appendix 5  Vehicle narrowband reference limits (Antenna-vehicle separation: 3 m)..................29 Appendix 6  Electrical/electronic sub-assembly (Broadband reference limits).............................30 Appendix 7  Electrical/electronic sub-assembly (Narrowband reference limits)...........................31

Annexes

Annex 1 Examples of approval marks....................................................................................32 Annex 2A Model of information document for type approval of a vehicle with respect to

electromahttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlgnetic compatibility...................................................................................33

Annex 2B Model of information document for type approval of an electric/electronic   sub-assembly with respect to electromagnetic compatibility.......................................38 Annex 3A Model of communication form for vehicle type approval.............................................39 Annex 3B Model of communication form for type approval of electrical/electronic

subassemblies .......................................................................................................41

Annex 4 Method of measurement of radiated broadband electromagnetic emissions from

vehicles..................................................................................................................43

Annex 4 - Appendix....................................................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.............................45 Annex 5 Method of measurement of radiated narrowband electromagnetic emissions from

vehicles..................................................................................................................49

Annex 6 Method of testing for immunity of vehicles to electromagnetic radiation......................51  Annex 6 - Appendix.................................................................................................56 Annex 7 Method of measurement of radiated broadband electromagnetic emissions from

electrical/electronic sub-assemblies.........................................................................60

Annex 7 - Appendix.................................................................................................62

Annex 8 Annex 9

Annex 10 Annex 11

Annex 12

Annex 13

Annex 14

Ahttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlnnex 15

Annex 16

Method of measurement of radiated narrowband electromagnetic emissions from

electrical/electronic sub-assemblies.........................................................................63 Method(s) of testing for immunity of electrical/electronic sub-assemblies to

electromagnetic radiation.........................................................................................65 Annex 9 - Appendix 1 Figures..................................................................................69 Annex 9 - Appendix 2 Typical TEM cell dimensions...................................................71 Method(s) of testing for immunity to and emission of transients of electrical/electronic  sub-assemblies.......................................................................................................72 Method(s) of testing for emission of transients of harmonics generated on AC://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html

power lines from vehicle..........................................................................................73 Annex 11 - Appendix 1............................................................................................74 Method(s) of testing for emission of voltage changes, voltage fluctuations and

flicker on AC power lines from vehicle......................................................................75 Annex 12 - Appendix 1............................................................................................76 Method(s) of testing for emission of radiofrequency conducted disturbances on

AC or DC power lines from vehicle...........................................................................77 Annex 13 - Appendix 1............................................................................................78 Method(s) of testing for emission of radiofrequency conducted disturbanchttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmles

on network and telecommunication access from vehicle............................................79 Annex 14 - Appendix 1............................................................................................80 Method(s) of testing for immunity of vehicles to electrical fast transient / burst

disturbances conducted along AC and DC power lines..............................................81 Annex 15 - Appendix 1............................................................................................83 Method(s) of testing for immunity of vehicles to surges conducted along AC

and DC power lines.................................................................................................84 Annex 16 - Appendix 1............................................................................................86

UNIFORM PROVISIONS CONCERNING THE APPROVAL OF VEHICLES://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlr

WITH REGARD TO ELECTROMAGNETIC COMPATIBILITY

1. SCOPE

This Regulation applies to:

1.1. vehicles of categories L, M, N and O 1) with regard to electromagnetic compatibility;  1.2. Components and separate technical units intended to be fitted in these vehicles with

the limitation given in paragraph 3.2.1. with regard to electromagnetic compatibility.

1.3. It covers:

(a) requirements regarding the immunity to radiated and conducted disturbances

for functions related to direct control of the vehicle, related to driver, passenger and other road users' protection, related to disturbances, which would cause confusion to the driver or other road users, related to vehicle data bus func-tionality, related to disturbances, which would affect vehicle statutory data;

(b) requirements regarding the control of unwanted radiated and conducted http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlemis-sions to protect the intended use of electrical or electronic equipment at own or adjacent vehicles or nearby, and the control of disturbances from accessories that may be retrofitted to the vehicle.

(c) additional requirements for vehicles providing coupling systems for charging

the RESS regarding the control of emissions and immunity from this connection between vehicle and power grid.

2. DEFINITIONS

For the purposes of this Regulation:

separate technical unit(s) to function satisfactorily in its electromagnetic environment without introducing intolerable electromagnetic disturbances to anything in that envi-ronment.

degrade the performance of a vehicle or component(s) or separate technical unit(s), or of any other device, unit of equipment or system operated in vicinity of a vehicle. An electromagnetic disturbance may be electromagnehttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmltic noise, an unwanted signal or a change in the propagation medium itself.

sepa-rate technical unit(s) to operate without degradation of performance in the presence

of (specified) electromagnetic disturbances which includes wanted radio frequency signals from radio transmitters or radiated in-band emissions of industrial-scientific-medical (ISM) apparatus, internal or external to the vehicle.

existing at a given location.

1)

As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document

TRANS/WP.29/Rev.1/Amend.2, as last amended by Amend.4).

of a particular measuring apparatus or receiver (International Special Committee on Radio Interference (CISPR) 25, second edition 2002 and corrigendum 2004).

particular measuring apparatus or receiver (CISPR 25, second edition 2002 anhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmld cor-rigendum 2004).

set(s) of devices together with any associated electrical connections which form part of a vehicle but which are not intended to be type approved separately from the vehi-cle. Both RESS and Coupling system for charging the RESS are considered electri-cal / electronic systems.

(ESA) means an electrical and/or electronic  device or set(s) of devices intended to be part of a vehicle, together with any associ-ated electrical connections and wiring, which performs one or more specialized func-tions. An ESA may be approved at the request of a manufacturer or his authorized representative as either a "component" or a "separate technical unit (STU)".

do not differ essentially in such respects as:

2.9.1. the overall size and shape of the engine compartment;

2.9.2. the general arrangement of the electrical and/or electronic comhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlponents and the

general wiring arrangement;

2.9.3. the primary material of which the body or shell  of the vehicle is constructed (for

example, a steel, aluminium or fiberglass body shell). The presence of panels of  different material does not change the vehicle type provided the primary material of the body is unchanged. However, such variations must be notified.

2.10. differ in such essential respects as:

2.10.1. the function performed by the ESA;

2.10.2. the general arrangement of the electrical and/or electronic components, if applicable.

active antenna cables, which are installed by the vehicle manufacturer.

(a) Functions related to the direct control of the vehicle:

(i) (ii) (iii) (b)

(i)

e.g. airbag and safety restraint systems.

by degradation or chttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlhange in: e.g. engine, gear, brake, suspension,  active steering, speed limitation devices;

by affecting driver’s position: e.g. seat or steering wheel positioning; by affecting driver's visibility: e.g. dipped beam, windscreen wiper.

Functions related to driver, passenger and other road user protection:

(c)

(i)

Functions which when disturbed cause confusion to the driver or other road users:

optical disturbances: incorrect operation of e.g. direction indicators, stop lamps, end outline marker lamps, rear position lamp, light bars for  emergency system, wrong information from warning indicators, lamps or displays related to functions in subparagraphs (a) or (b) which might be observed in the direct view of the driver;

acoustical disturbances: incorrect operation of e.g. anti-theft alarm, horn.

(ii)

(d)://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlar

(i)

(e)

(f)

(i)

Functions related to vehicle data bus functionality:

by blocking data transmission on vehicle data bus-systems, which are used to transmit data, required to ensure the correct functioning of other immunity related functions.

Functions which when disturbed affect vehicle statutory data: e.g. tachograph, odometer.

Function related to the RESS in charging mode coupled to the power grid:

by leading to unexpected vehicle motion.

for electric propulsion of the vehicle.

2.14. vehicle used for charging the RESS.

3. APPLICATION FOR APPROVAL  3.1. Approval of a vehicle type

3.1.1. The application for approval of a vehicle type, with regard to its electromagnetic

compatibility, shall be submitted by the vehicle manufacturerhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.

3.1.2. A model of information document is shown in Annex 2A.

3.1.3. The vehicle manufacturer shall draw up a schedule describing all relevant vehicle

electrical/electronic systems or ESAs, body styles, variations in body material, gen-eral wiring arrangements, engine variations, left-hand/right-hand drive versions and wheelbase versions. Relevant vehicle electrical/electronic systems or ESAs are those which may emit significant broadband or narrowband radiation and/or those which are involved in immunity related functions of the vehicle (see paragraph 2.12.) and those which provide coupling systems for charging the RESS.

3.1.4. A vehicle representative of the type to be approved shall be selected from this

schedule by mutual agreement between the manufacturer and the Competent Author-ity. The choice of vehicle shall be based on the electrical/electronic systehttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlms offered by the manufacturer. One or more vehicles may be selected from this schedule if it is considered by mutual agreement between the manufacturer and the Competent  Authority that different electrical/electronic systems are included which are likely to have a significant effect on the vehicle's electromagnetic compatibility compared with the first representative vehicle.

3.1.5. The choice of the vehicle(s) in conformity with paragraph 3.1.4. above shall be

limited to vehicle/electrical/electronic system combinations intended for actual  production.

3.1.7.

3.1.8.

been carried out. Any such data provided may be used by the approval authority for the purpose of drawing up the communication form for type-approval.

If the Technical Service responsible for the type approval test carries out the test itself, then a vehicle representative of the type tohttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html be approved according to  paragraph 3.1.4. shall be provided.

For vehicles of categories M, N, and O the vehicle manufacturer must provide a statement of frequency bands, power levels, antenna positions and installation provi-sions for the installation of radio frequency transmitters (RF-transmitters), even if the vehicle is not equipped with an RF transmitter at time of type approval. This should cover all mobile radio services normally used in vehicles. This information must be made publicly available following the type approval.

Vehicle manufacturers must provide evidence that vehicle performance is not ad-versely affected by such transmitter installations.

3.1.9. Vehicle type approval shall be applied for both RESS and Coupling system for

charging the RESS as they are considered as electrical / electronic systems.

3.2. ESA type approval

3.2.1. Apphttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmllicability of this Regulation to ESA:

3.2.3.

3.2.4.

3.2.5.

patibility shall be submitted by the vehicle manufacturer or by the manufacturer of the ESA.

A model of information document is shown in Annex 2B.

The manufacturer may supplement the application with a report on tests which have been carried out. Any such data provided may be used by the approval authority for the purpose of drawing up the communication form for type-approval.

If the Technical Service responsible for the type approval test carries out the test itself, then a sample of the ESA system representative of the type to be approved shall be provided, if necessary, after discussion with the manufacturer on, e.g., pos-sible variations in the layout, number of components, number of sensors. If the Technical Service deems it necessary, it may select a further sample.

The http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlsample(s) must be clearly and indelibly marked with the manufacturer's trade name or mark and the type designation.

Where applicable, any restrictions on use should be identified. Any such restrictions should be included in Annexes 2B and/or 3B.

ESA which are brought to the market as spare parts need no type approval if they are obviously marked as a spare part by an identification number and if they are identical and from the same manufacturer as the corresponding original equipment manufacturer (OEM) part for an already type approved vehicle.

Components sold as aftermarket equipment and intended for the installation in motor vehicles need no type approval if they are not related to immunity related functions (see paragraph 2.12.). In this case a declaration must be issued by the manufacturer that the ESA fulfils the requirements of this Regulation and in particular the limits  defined in paragraphshttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html 6.5., 6.6., 6.8. and 6.9.

3.2.6.

3.2.7.

3.2.8.

3.2.9.

4. APPROVAL  4.1. Type approval procedures

4.1.1. Type approval of a vehicle

The following alternative procedures for vehicle type approval may be used at the discretion of the vehicle manufacturer.

4.1.1.1. Approval of a vehicle installation

A vehicle installation may be type approved directly by following the provisions laid down in paragraph 6 of this Regulation. If this procedure is chosen by a vehicle manufacturer, no separate testing of electrical/electronic systems or ESAs is re-quired.

4.1.1.2. Approval of vehicle type by testing of individual ESAs

A vehicle manufacturer may obtain approval for the vehicle by demonstrating to the approval authority that all the relevant (see para. 3.1.3. of this Regulation)  electhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlrical/electronic systems or ESAs have been approved in accordance with this Regulation and have been installed in accordance with any conditions attached thereto.

4.1.1.3. A manufacturer may obtain approval according to this Regulation if the vehicle has

no equipment of the type, which is subject to immunity or emission tests. Such  approvals do not require testing.

4.1.2. Type approval of an ESA

Type approval may be granted to an ESA to be fitted either to any vehicle type  (component approval) or to a specific vehicle type or types requested by the ESA manufacturer (separate technical unit approval).

4.1.3. ESAs, which are intentional RF transmitters, which have not received type approval

in conjunction with a vehicle manufacturer, must be supplied with suitable installation guidelines.

4.2. Granting of type approval

4.2.http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html1. Vehicle

4.2.1.1. If the representative vehicle fulfils the requirements of paragraph 6 of this Regula-tion, type approval shall be granted.

4.2.1.2. A model of communication form for type approval is contained in Annex 3A.

4.2.2. ESA

4.2.2.1. If the representative ESA system(s) fulfil(s) the requirements of paragraph 6 of this

Regulation, type approval shall be granted.

4.2.2.2. A model of communication form for type approval is contained in Annex 3B.

4.2.3. In order to draw up the communication forms referred to in paragraph 4.2.1.2. or

4.2.2.2. above, the Competent Authority of the Contracting Party granting the  approval may use a report prepared or approved by a recognized laboratory or in  accordance with the provisions of this Regulation.

4.3. Approval, or refusal of approval, of a type of vehicle or ESA in accordanchttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmle with this

Regulation shall be notified to the Parties to the Agreement applying this Regulation on a form conforming to the model in Annex 3A or 3B of this Regulation, accompa-nied by photographs and/or diagrams or drawings on an appropriate scale supplied by the applicant in a format not larger than A4 (210 x 297 mm) or folded to those  dimensions.

5. MARKINGS  5.1. An approval number shall be assigned to each vehicle or ESA type approved. The

first two digits of this number shall indicate the series of amendments corresponding to the most recent essential technical amendments made to the Regulation at the date of approval. A Contracting Party may not assign the same approval number to another type of vehicle or ESA.

5.2. Presence of markings

5.2.1. Vehicle

An approval mark described in paragraph 5.3. below shall be affixed to every vehicle conformihttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlng to a type approved under this Regulation.

5.2.2. Sub-assembly

An approval mark described in paragraph 5.3. below shall be affixed to every ESA conforming to a type approved under this Regulation.

No marking is required for electrical/electronic systems built into vehicles which are approved as units.

5.3. An international approval mark must be affixed, in a conspicuous and easily accessi-ble place specified on the approval communication form, on each vehicle conforming

to the type approved under this Regulation. This mark shall comprise:

5.3.1. A circle containing the letter "E", followed by the distinguishing number of the country

2)

granting the approval.

5.3.2. The number of this Regulation, followed by the letter "R", a dash and the approval

number to the right of the circle specified in http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlparagraph 5.3.1.

5.4. An example of the type-approval mark is shown in Annex 1 to this Regulation.  5.5. Markings on ESAs in conformity with paragraph 5.3. above need not be visible when

the ESA is installed in the vehicle.

6. SPECIFICATIONS IN CONFIGURATIONS OTHER THAN “RESS CHARGING MODE

COUPLED TO THE POWER GRID”

6.1. General specifications

6.1.1. A vehicle and its electrical/electronic system(s) or ESA(s) shall be so designed,

constructed and fitted as to enable the vehicle, in normal conditions of use, to com-ply with the requirements of this Regulation.

6.1.1.1. A vehicle shall be tested for radiated emissions and for immunity to radiated distur-bances. No tests for conducted emissions or immunity to conducted disturbances are required for vehicle type approval.

6.1.1.2. ESA(s) shall be tested for http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlradiated and conducted emissions, for immunity to

radiated and conducted disturbances.

6.1.2. Before testing the Technical Service has to prepare a test plan in conjunction with

the manufacturer, which contains at least mode of operation, stimulated function(s), monitored function(s), pass/fail criterion(criteria) and intended emissions.

2)

1 for Germany, 2 for France, 3 for Italy, 4 for the Netherlands, 5 for Sweden, 6 for Belgium, 7 for Hungary, 8 for

the Czech Republic, 9 for Spain, 10 for Serbia, 11 for the United Kingdom, 12 for Austria, 13 for Luxembourg, 14 for Switzerland, 15 (vacant), 16 for Norway, 17 for Finland, 18 for Denmark, 19 for Romania, 20 for Poland, 21 for Portugal, 22 for the Russian Federation, 23 for Greece, 24 for Ireland, 25 for Croatia, 26 for Slovenia, 27 for Slovakia, 28 for Belarus, 29 for Estonia, 30 (vacant), 31 for Bosnhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlia and Herzegovina, 32 for Latvia, 33 (vacant), 34 for Bulgaria, 35 (vacant), 36 for Lithuania, 37 for Turkey, 38 (vacant), 39 for Azerbaijan, 40 for The former Yugoslav Republic of Macedonia, 41 (vacant), 42 for the European Community (Approvals are granted by its Member States using their respective ECE symbol), 43 for Japan, 44 (vacant), 45 for Australia, 46 for Ukraine, 47 for South Africa, 48 for New Zealand, 49 for Cyprus, 50 for Malta, 51 for the Republic of Ko-rea, 52 for Malaysia, 53 for Thailand, 54 and 55 (vacant), 56 for Montenegro, 57 (vacant) and 58 for Tunisia. Subsequent numbers shall be assigned to other countries in the chronological order in which they ratify or ac-cede to the Agreement Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Recipro-cal Recognition of Approvals Granted ohttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmln the Basis of these Prescriptions, and the numbers thus assigned shall be communicated by the Secretary-General of the United Nations to the Contracting Parties to the Agreement.

6.2. Specifications concerning broadband electromagnetic radiation from vehicles

6.2.1. Method of measurement

The electromagnetic radiation generated by the vehicle representative of its type shall be measured using the method described in Annex 4. The method of measure-ment shall be defined by the vehicle manufacturer in accordance with the Technical Service.

6.2.2. Vehicle broadband type approval limits

6.2.2.1. If measurements are made using the method described in Annex 4 using a

vehicle-to-antenna spacing of 10.0 ± 0.2 m, the limits shall be 32 dB microvolts/m in the 30 to 75 MHz frequency band and 32 to 43 dB microvolts/m in the 75 to 400 MHz frequency band, this limit http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlincreasing logarithmically with frequencies above 75 MHz as shown in Appendix 2. In the 400 to 1,000 MHz frequency band the limit remains constant at 43 dB microvolts/m.

6.2.2.2. If measurements are made using the method described in Annex 4 using a vehicle-to-antenna spacing of 3.0 ± 0.05 m, the limits shall be 42 dB microvolts/m in the 30 to 75 MHz frequency band and 42 to 53 dB microvolts/m in the 75 to 400 MHz frequency band, this limit increasing logarithmically with frequencies above 75 MHz as shown in Appendix 3. In the 400 to 1,000 MHz frequency band the limit remains constant at 53 dB microvolts/m.

6.2.2.3. On the vehicle representative of its type, the measured values, expressed in dB

microvolts/m shall be below the type approval limits.

6.3. Specifications concerning narrowband electromagnetic radiation from vehicles

6.3.1. Method of measurement

://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlparThe electromagnetic radiation generated by the vehicle representative of its type shall be measured using the method described in Annex 5. These shall be defined by the vehicle manufacturer in accordance with the Technical Service.

6.3.2. Vehicle narrowband type approval limits

6.3.2.1. If measurements are made using the method described in Annex 5 using a vehicle-to-antenna spacing of 10.0 ± 0.2 m, the limits shall be 22 dB microvolts/m in the 30 to 75 MHz frequency band and 22 to 33 dB microvolts/m in the 75 to 400 MHz frequency band, this limit increasing logarithmically with frequencies above 75 MHz as shown in Appendix 4. In the 400 to 1,000 MHz frequency band the limit remains constant at 33 dB microvolts/m.

6.3.2.2. If measurements are made using the method described in Annex 5 using a vehicle-to-antenna spacing of 3.0 ± 0.05 m, the limit shall be 32 dB microvolts/m http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlin the 30 to 75 MHz frequency band and 32 to 43 dB microvolts/m in the 75 to 400 MHz  frequency band, this limit increasing logarithmically with frequencies above 75 MHz as shown in Appendix 5. In the 400 to 1,000 MHz frequency band the limit remains constant at 43 dB microvolts/m.

6.3.2.3. On the vehicle representative of its type, the measured values, expressed in dB

microvolts/m, shall be below the type approval limit.

6.3.2.4. Notwithstanding the limits defined in paragraphs 6.3.2.1., 6.3.2.2. and 6.3.2.3. of this

Regulation, if, during the initial step described in paragraph 1.3. of Annex 5, the  signal strength measured at the vehicle broadcast radio antenna is less than 20 dB micro-volts over the frequency range 76 to 108 MHz measured with an average

detector, then the vehicle shall be deemed to comply with the limits for narrowband emissions and no furthttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlher testing will be required.

6.4. Specifications concerning immunity of vehicles to electromagnetic radiation

6.4.1. Method of testing

The immunity to electromagnetic radiation of the vehicle representative of its type shall be tested by the method described in Annex 6.

6.4.2. Vehicle immunity type approval limits

6.4.2.1. If tests are made using the method described in Annex 6, the field strength shall be

30 volts/m rms (root mean squared) in over 90 per cent of the 20 to 2,000 MHz  frequency band and a minimum of 25 volts/m rms over the whole 20 to 2,000 MHz frequency band.

6.4.2.2. The vehicle representative of its type shall be considered as complying with immunity

requirements if, during the tests performed in accordance with Annex 6, there shall be no degradation of performance of "immunity related functions", according to parahttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html-graph 2.1. of Annex 6.

6.5. Specification concerning broadband electromagnetic interference generated by

ESAs.

6.5.1. Method of measurement

The electromagnetic radiation generated by the ESA representative of its type shall be measured by the method described in Annex 7.

6.5.2. ESA broadband type approval limits

6.5.2.1. If measurements are made using the method described in Annex 7, the limits shall be

62 to 52 dB microvolts/m in the 30 to 75 MHz frequency band, this limit decreasing logarithmically with frequencies above 30 MHz, and 52 to 63 dB microvolts/m in the 75 to 400 MHz band, this limit increasing logarithmically with frequencies above 75 MHz as shown in Appendix 6. In the 400 to 1,000 MHz frequency band the limit remains constant at 63 dB microvolts/m.

6.5.2.2. On the ESA representative of its type, thttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlhe measured values, expressed in dB micro-volts/m, shall be below the type approval limits.

6.6. Specifications concerning narrowband electromagnetic interference generated by

ESAs.

6.6.1. Method of measurement

The electromagnetic radiation generated by the ESA representative of its type shall be measured by the method described in Annex 8.

6.6.2. ESA narrowband type approval limits

6.6.2.1. If measurements are made using the method described in Annex 8, the limits shall be

52 to 42 dB microvolts/m in the 30 to 75 MHz frequency band, this limit decreasing logarithmically with frequencies above 30 MHz, and 42 to 53 dB microvolts/m in the 75 to 400 MHz band, this limit increasing logarithmically with frequencies above 75 MHz as shown in Appendix 7. In the 400 to 1,000 MHz frequency band the limit remains constant at 53 dB microvolts/mhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.

6.6.2.2. On the ESA representative of its type, the measured value, expressed in dB micro-volts/m shall be below the type approval limits.

6.7. Specifications concerning immunity of ESAs to electromagnetic radiation

6.7.1. Method(s) of testing

The immunity to electromagnetic radiation of the ESA representative of its type shall be tested by the method(s) chosen from those described in Annex 9.

6.7.2. ESA immunity type approval limits

6.7.2.1. If tests are made using the methods described in Annex 9, the immunity test levels

shall be 60 volts/m root-mean-square (rms) for the 150 mm stripline testing method, 15 volts/m rms for the 800 mm stripline testing method, 75 volts/m rms for the Transverse Electromagnetic Mode (TEM) cell testing method, 60 mA rms for the bulk current injection (BCI) testing method and 30 volts/m rms for the free field  http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmltesting method in over 90 per cent of the 20 to 2,000 MHz frequency band, and to a minimum of 50 volts/m rms for the 150 mm stripline testing method, 12.5 volts/m rms for the 800 mm stripline testing method, 62.5 volts/m rms, for the TEM cell testing method, 50 mA rms for the bulk current injection (BCI) testing method and 25 volts/m rms for the free field testing method over the whole 20 to 2,000 MHz frequency band.

6.7.2.2. The ESA representative of its type shall be considered as complying with immunity

requirements if, during the tests performed in accordance with Annex 9, there shall be no degradation of performance of "immunity related functions".

6.8. Specifications concerning the immunity of ESAs to transient disturbances conducted

along supply lines.

6.8.1. Method of testing

The immunity of ESA representative of its type shall be tested by thehttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html method(s)  according to ISO 7637-2 (second edition 2004 and Amd1:2008) as described in  Annex 10 with the test levels given in table 1.

Immunity of ESA

Test pulse number 1 2a 2b 3a/3b 4

Immunity  test level

III III III III III

Functional status for systems:

Related to immunity  related functions C B C A B

(for ESA which must be operational during engine

start phases)

C

(for other ESA)

Not related to immunity

related functions

D D D D D

6.9.

Specifications concerning the emission of transient conducted disturbances gener-ated by ESAs on supply lines.

6.9.1. Method of testing

The emission of ESA representative of its type shall be tested by the method(s)  according to ISO 7637-2 (second edition 2004 and Amd1:2008) as described in  Annex 10 for thttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlhe levels given in table 2.

Maximum allowed pulse amplitude  *)

Polarity of pulse

amplitude Positive Negative

Maximum allowed pulse amplitude for

Vehicles with 12 V systems

75 -100

Vehicles with 24 V systems

150 -450

6.10. Exceptions

6.10.1. Where a vehicle or electrical/electronic system or ESA does not include an electronic

oscillator with an operating frequency greater than 9 kHz, it shall be deemed to  comply with paragraph 6.3.2. or 6.6.2. and with Annexes 5 and 8.

6.10.2. Vehicles which do not have electrical/electronic systems with "immunity related func-tions" need not be tested for immunity to radiated disturbances and shall be deemed to comply with paragraph 6.4. and with Annex 6 to this Regulation.

6.10.3. ESAs with no immunity related functionshttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html need not be tested for immunity to radiated

disturbances and shall be deemed to comply with paragraph 6.7. and with Annex 9 to this Regulation.

6.10.4. Electrostatic discharge

For vehicles fitted with tyres, the vehicle body/chassis can be considered to be an electrically isolated structure. Significant electrostatic forces in relation to the  vehicle's external environment only occur at the moment of occupant entry into or exit from the vehicle. As the vehicle is stationary at these moments, no type approval test for electrostatic discharge is deemed necessary.

6.10.5. Emission of transient conducted disturbances generated by ESAs on supply lines.   ESAs that are not switched, contain no switches or do not include inductive loads

need not be tested for transient conducted emission and shall be deemed to comply with paragraph 6.9.

6.10.6. Thttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlhe loss of function of receivers during the immunity test, when the test signal is

within the receiver bandwidth (RF exclusion band) as specified for the specific radio service/product in the harmonized international EMC standard, does not necessarily lead to a fail criteria **).

*)

ALO editorial note: Table 2 should obviously remain within the Regulation (notwithstanding the amendments as

per document TRANS/WP.29/2011/8)  ALO editorial note: should obviously read “fail criterion“

**)

6.10.7. RF transmitters shall be tested in the transmit mode. Wanted emissions (e.g. from

RF transmitting systems) within the necessary bandwidth and out of band emissions are disregarded for the purpose of this Regulation. Spurious emissions are subject to this Regulation.

6.10.7.1. "Necessary Bandwidth": for a given class of emisshttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlion, the width of the frequency

band which is just sufficient to ensure the transmission of information at the rate and with the quality required under specified conditions (Article 1, No. 1.152 of the Inter-national Telecommunication Union (ITU) Radio Regulations).

6.10.7.2. "Out-of-band Emissions": Emission on a frequency or frequencies immediately

outside the necessary bandwidth which results from the modulation process, but  excluding spurious emissions (Article 1, No. 1.144 of the ITU Radio Regulations).

6.10.7.3. "Spurious Emission": In every modulation process additional undesired signals exist.

They are summarized under the expression "spurious emissions". Spurious emis-sions are emissions on a frequency or frequencies, which are outside the necessary bandwidth and the level of which may be reduced without affecting the corresponding transmission of infhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlormation. Spurious emissions include harmonic emissions, para-sitic emissions, intermodulation products and frequency conversion products, but  exclude out-of-band emissions (Article 1 No. 1.145 of the ITU Radio Regulations).

7. ADDITIONAL SPECIFICATIONS IN THE CONFIGURATION “RESS CHARGING

MODE COUPLED TO THE POWER GRID”

7.1. General specifications

7.1.1. A vehicle and its electrical/electronic system(s) shall be so designed, constructed

and fitted as to enable the vehicle, in configuration "RESS charging mode coupled to the power grid", to comply with the requirements of this Regulation.

7.1.2. A vehicle in configuration "RESS charging mode coupled to the power grid" shall be

tested for radiated emissions, immunity to radiated disturbances, conducted emis-sions and immunity to conducted disturbances.

7.1.3. Before testing http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlthe Technical Service has to prepare a test plan in conjunction with

the manufacturer, for the configuration "RESS charging mode coupled to the power

*)

grid" configuration  which contains at least mode of operation, stimulated func-tion(s), monitored function(s), pass/fail criterion (criteria) and intended emissions.

7.2. Specifications concerning broadband electromagnetic radiation from vehicles

7.2.1. Method of measurement

The electromagnetic radiation generated by the vehicle representative of its type shall be measured using the method described in Annex 4. The method of measure-ment shall be defined by the vehicle manufacturer in accordance with the Technical Service.

7.2.2. Vehicle broadband type approval limits

7.2.2.1. If measurements are made using the method described in Annex 4 using a vehicle-to-antenna spacing of 10.0 ± 0.2 m, the limits shalhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmll be 32 dB microvolts/m in the 30 to 75 MHz frequency band and 32 to 43 dB microvolts/m in the 75 to 400 MHz frequency band, this limit increasing logarithmically with frequencies above 75 MHz as shown in Appendix 2. In the 400 to 1,000 MHz frequency band the limit remains constant at 43 dB microvolts/m.

*)

ALO editorial note: “configuration“ listed twice

7.2.2.2. If measurements are made using the method described in Annex 4 using a vehicle-to-antenna spacing of 3.0 ± 0.05 m, the limits shall be 42 dB microvolts/m in the 30 to 75 MHz frequency band and 42 to 53 dB microvolts/m in the 75 to 400 MHz frequency band, this limit increasing logarithmically with frequencies above 75 MHz as shown in Appendix 3. In the 400 to 1,000 MHz frequency band the limit remains constant at 53 dB microvolts/m.

On the vehicle representative of its type, the measured values, exprhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlessed in dB microvolts/m shall be below the type approval limits.

7.3. Specifications concerning emission of harmonics on AC power lines from vehicles

7.3.1. Method of measurement  The harmonics emission on AC power lines generated by the vehicle representative

of its type shall be measured using the method described in Annex 11. The method of measurement shall be defined by the vehicle manufacturer in accordance with the Technical Service.

7.3.2. Vehicle type approval limit

7.3.2.1. If measurements are made using the method described in Annex 11, the limits for

input current ≤ 16 A per phase are those defined in IEC 61000-3-2 (edition 3.2 – 2005   Amd1:2008   Amd2:2009) and given in table 3.

Table 3

Maximum allowed harmonics (input current ≤ 16 A per phase)

Harmonic number Maximum authorized harmonic current

://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlarn A

Odd harmonics

3 2.3 5 1.14 7 0.77 9 0.40 11 0.33 13 0.21 15 ≤ n ≤ 39 0.15x15/n

Even harmonics

2 1.08 4 0.43 6 0.30 8 ≤ n ≤ 40 0.23x8/n

7.3.2.2. If measurements are made using the method described in Annex 11, the limits for

input current > 16 A and ≤ 75 A per phase are those defined in IEC 61000-3-12 (edi-tion 1.0 - 2004) and given in table 4, 5 and 6.

Table 4

Maximum allowed harmonics (input current > 16 A and ≤ 75 A per phase)

for equipment other than balanced three-phase equipment

Minimum Rsce

Acceptable individual harmonic current In/I1 %

Maximum current harmonic

ratio %

I3 I5 I7 I9 I11 I13 THD PWHD 33 21.6 10.7 7.2 3.8 3.1 2 23 23 66 24 13 8 5 4 3 26 26 120 27 15 10 6 5 4 30 30 250 35 20 13 9 8 6 40 40 ≥ 350 41 24 15 12 10 8 47 47

Relative values ofhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html even harmonics lower or equal to 12 shall be lower than 16/n %. Even harmonics greater than 12 are taken into account in the THD and PWHD the same way than odd harmonics.

Linear interpolation between successive values of Rsce is authorized.

Table 5

Maximum allowed harmonics (input current > 16 A and ≤ 75 A per phase)

for balanced three-phase equipment

Minimum Acceptable individual harmonic Maximum current harmonic ratio Rsce current In/I1 % %

I5 I7I11I13THD PWHD

3310.7 7.23.1213 226614 95316 2512019 127422 2825031 2012737 38≥ 35040 25151048 46

Relative values of even harmonics lower or equal to 12 shall be lower than 16/n %. Even harmonics greater than 12 are taken into account in the THD and PWHD the same way than odd harmonics.

Linear interpolation between successive values of Rsce is authorized.

Table 6

Maximum allhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlowed harmonics (input current > 16 A and ≤ 75 A per phase)

for balanced three-phase equipment under specific conditions

Minimum Rsce

Acceptable individual harmonic Maximum current harmonic

current In/I1 % ratio %

I5I7I11I13THD PWHD

33 10.77.23.1213 22≥ 120 4025151048 46

Relative values of even harmonics lower or equal to 12 shall be lower than 16/n %. Even harmonics greater than 12 are taken into account in the THD and PWHD the same way than odd harmonics

7.4.

Specifications concerning emission of voltage changes, voltage fluctuations and flicker on AC power lines from vehicles.

7.4.1. Method of measurement  The emission of voltage changes, voltage fluctuations and flicker on AC power lines

generated by the vehicle representative of its type shall be measured using the method described in Annex 12. The methohttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmld of measurement shall be defined by the vehicle manufacturer in accordance with the Technical Service.

7.4.2. Vehicle type approval limit

7.4.2.1. If measurements are made using the method described in Annex 12, the limits for

rated current ≤ 16 A per phase and not subjected to conditional connection are those defined in IEC 61000-3-3 (edition 2.0 - 2008) and given in table 7.

Table 7

Maximum allowed voltage changes, voltage fluctuations and flicker

(rated current ≤ 16 A per phase and not subjected to conditional connection)

Limits

Values given in 61000-3-3 clause 5

7.4.2.2. If measurements are made using the method described in Annex 12, the limits for

rated current > 16 A and ≤ 75 A per phase and subjected to conditional connection are those defined in IEC 61000-3-11 (edition 1.0 - 2000) and given in table 8.

Table http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html8

Maximum allowed voltage changes, voltage fluctuations and flicker

(rated current > 16 A and ≤ 75 A per phase and subjected to conditional connection)

Limits

Values given in IEC 61000-3-11 (edition 1.0 – 2000), clause 5   7.5. Specifications concerning emission of radiofrequency conducted disturbances on AC

or DC power lines from vehicles

7.5.1. Method of measurement  The emission of radiofrequency conducted disturbances on AC or DC power lines

generated by the vehicle representative of its type shall be measured using the method described in Annex 13. The method of measurement shall be defined by the vehicle manufacturer in accordance with the Technical Service.

7.5.2. Vehicle type approval limit

7.5.2.1. If measurements are made using the method described in Annex 13, the limits on AC

power lines are those definedhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html in IEC 61000-6-3 (edition 2.0 – 2006) and given in  table 9.

Table 9

Maximum allowed radiofrequency conducted disturbances on AC power lines

Frequency (MHz) Limits and detector 0.15 to 0.5  66 to 56 dB?V (quasi-peak) 56 to 46 dB?V

(average)

(linearly decreasing with logarithm of fre-quency)

0.5 to 5 56 dB?V (quasi-peak) 46 dB?V (average) 5 to 30 60 dB?V (quasi-peak) 50 dB?V (average)

7.5.2.2 If measurements are made using the method described in Annex 13, the limits on DC

power lines are those defined in IEC 61000-6-3 (edition 2.0 - 2006) and given in  table 10.

Table 10

Maximum allowed radiofrequency conducted disturbances on DC power lines

Frequency (MHz) 0.15 to 0.5  0.5 to 30

7.6.

Limits and detector 79 dB?V (quasi-peak)  66 dB?V (average) 73 dB?V (quasi-peak)  60 dB?V (averhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlage)

Specifications concerning emission of radiofrequency conducted disturbances on network and telecommunication access from vehicles

7.6.1. Method of measurement  The emission of radiofrequency conducted disturbances on network and telecommu-nication access generated by the vehicle representative of its type shall be measured

using the method described in Annex 14. The method of measurement shall be  defined by the vehicle manufacturer in accordance with the Technical Service.

7.6.2. Vehicle type approval limit

7.6.2.1. If measurements are made using the method described in Annex 14, the limits on

network and telecommunication access are those defined in IEC 61000-6-3 (edition 2.0 - 2006) and given in table 11.

Table 11

Maximum allowed radiofrequency conducted disturbances

on network and telecommunication access://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlpar

Frequency (MHz) Limits and detector 0.15 to 0.5  84 to 74 dB?V (quasi-40 to 30 dB?A (quasi-peak)

peak) 74 to 64 dB?V 30 to 20 dB?A (average) (line-(average) (linearly de-arly decreasing with logarithm creasing with logarithm of frequency) of frequency)

0.5 to 30 74 dB?V (quasi-peak)  30 dB?A (quasi-peak)

64 dB?V (average) 20 dB?A (average)

7.7. Specifications concerning immunity of vehicles to electromagnetic radiation

7.7.1. Method of testing  The immunity to electromagnetic radiation of the vehicle representative of its type

shall be tested by the method described in Annex 6.

7.7.2. Vehicle immunity type approval limits

7.7.2.1. If tests are made using the method described in Annex 6, the field strength shall

be 30 volts/m rms (root mean squared) in over 90 per cent of the 20 to 2,000 MHz frequency band and a minimhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlum of 25 volts/m rms over the whole 20 to 2,000 MHz frequency band.

7.7.2.2. The vehicle representative of its type shall be considered as complying with immunity

requirements if, during the tests performed in accordance with Annex 6, there shall be no degradation of performance of "immunity related functions", according to para-graph 2.2. of Annex 6.

7.8.

Specifications concerning the immunity of vehicles to electrical fast transient/burst disturbances conducted along AC and DC power lines.

7.8.1. Method of testing

7.8.1.1. The immunity to electrical fast transient/burst disturbances conducted along AC and

DC power lines of the vehicle representative of its type shall be tested by the method described in Annex 15.

7.8.2. Vehicle immunity type approval limits

7.8.2.1. If tests are made using the methods http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmldescribed in Annex 15, the immunity test levels,

for AC or DC power lines, shall be : ± 2 kV test voltage in open circuit, with a rise time (Tr) of 5 ns, and a hold time (Th) of 50 ns and a repetition rate of 5 kHz for at least 1 minute.

7.8.2.2. The vehicle representative of its type shall be considered as complying with immunity

requirements if, during the tests performed in accordance with Annex 15, there shall be no degradation of performance of "immunity related functions", according to para-graph 2.2. of Annex 6."

7.9. Specifications concerning the immunity of vehicles to surge conducted along AC or

DC power lines.

7.9.1. Method of testing

7.9.1.1. The immunity to surge conducted along AC / DC power lines of the vehicle represen-tative of its type shall be tested by the method described in Annex 16.

7.9.2. Vehicle immhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlunity type approval limits

7.9.2.1. If tests are made using the methods described in Annex 16, the immunity test levels

shall be:

(a) for AC power lines: ± 2 kV test voltage in open circuit between line and earth and

± 1 kV between lines, with a rise time (Tr) of 1,2 ?s, and a hold time (Th) of 50 ?s. Each surge shall be applied 5 times at 1 minute delay for each of following phases: 0, 90, 180 and 270°,

(b)  for DC power lines: ± 0,5 kV test voltage in open circuit between line and earth and

± 0,5 kV between lines, with a rise time (Tr) of 1,2 ?s, and a hold time (Th) of 50 ?s. Each surge shall be applied 5 times at 1 minute delay.

7.9.2.2. The vehicle representative of its type shall be considered as complying with immunity

requirements if, during the tests performed in accordance with Annex 16, there shall be no degradation of performance of http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html"immunity related functions", according to para-graph 2.2. of Annex 6.

7.10. Exceptions

7.10.1. When network and telecommunication access of the vehicle uses power line Trans-mission (PLT) on its AC/DC power lines, annex 14 shall not be applied.

8.  8.1.

AMENDMENT OR EXTENSION OF A VEHICLE TYPE APPROVAL FOLLOWING ELECTRICAL/ELECTRONIC SUB-ASSEMBLY (ESA) ADDITION OR SUBSTITU-TION

Where a vehicle manufacturer has obtained type approval for a vehicle installation and wishes to fit an additional or substitutional electrical/electronic system or ESA which has already received approval under this Regulation, and which will be in-stalled in accordance with any conditions attached thereto, the vehicle approval may be extended without further testing. The additional or substitutional  electrical/electronic system or ESA shall be considered as part of the vehicle for  cohttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlnformity of production purposes.

Where the additional or substitutional part(s) has (have) not received approval  pursuant to this Regulation, and if testing is considered necessary, the whole vehicle shall be deemed to conform if the new or revised part(s) can be shown to conform to the relevant requirements of paragraph 6 or if, in a comparative test, the new part can be shown not to be likely to adversely affect the conformity of the vehicle type. The addition by a vehicle manufacturer to an approved vehicle of standard domestic or business equipment, other than mobile communication equipment, which conforms to other regulations, and the installation, substitution or removal of which is accord-ing to the recommendations of the equipment and vehicle manufacturers, shall not invalidate the vehicle approval. This shall not preclude vehicle manufacturers fitting communication equipment in accordance with suitable instahttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlllation guidelines devel-oped by the vehicle manufacturer and/or manufacturer(s) of such communication equipment. The vehicle manufacturer shall provide evidence (if requested by the test authority) that vehicle performance is not adversely affected by such transmitters. This can be a statement that the power levels and installation are such that the  immunity levels of this Regulation offer sufficient protection when subject to  transmission alone i.e. excluding transmission in conjunction with the tests specified in paragraph 6. This Regulation does not authorize the use of a communication transmitter when other requirements on such equipment or its use apply. CONFORMITY OF PRODUCTION

The conformity of production procedures shall comply with those set out in the Agreement, Appendix 2 (E/ECE/324-E/ECE/TRANS/505/Rev.2), with the following requirements:

8.2.

8.3.

9.

9.1.  http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html9.2.  9.3.

9.3.1.

Vehicles or components or ESAs approved under this Regulation shall be so manu-factured as to conform to the type approved by meeting the requirements set forth in paragraph 6 above.

Conformity of production of the vehicle or component or separate technical unit shall be checked on the basis of the data contained in the communication form(s) for type approval set out in Annex 3A and/or 3B of this Regulation.

If the Competent Authority is not satisfied with the checking procedure of the manu-facturer, then paragraphs 8.3.1. and 8.3.2. below shall apply.

When the conformity of a vehicle, component or ESA taken from the series is being verified, production shall be deemed to conform to the requirements of this Regula-tion in relation to broadband electromagnetic disturbances and narrowband electro-magnetic disturbances if the levels measured do not exceed by more the http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html*) 2 dB (25 per cent) the reference limits prescribed in paragraphs 6.2.2.1., 6.2.2.2., 6.3.2.1., 6.3.2.2., 7.2.2.1. and 7.2.2.2. (as appropriate).

*)

ALO editorial note: should obviously read “by more than“

9.3.2.

When the conformity of a vehicle, component or ESA taken from the series is being verified, production shall be deemed to conform to the requirements of this Regula-tion in relation to immunity to electromagnetic radiation if the vehicle ESA does not exhibit any degradation relating to the direct control of the vehicle which could be observed by the driver or other road user when the vehicle is in the state defined in Annex 6, para. 4, and is subjected to a field strength, expressed in Volts/m, up to 80 per cent of the reference limits prescribed in paragraphs 6.4.2.1. and 7.7.2.1. above. If the conformity of a component, or Separate Technical Unit (STU) takehttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmln from the series is being verified, production shall be deemed to conform to the requirements of this Regulation in relation to immunity to conducted disturbances and emission if the component or STU shows no degradation of performance of "immunity related functions" up to levels given in paragraph 6.8.1. and does not exceed the levels given in paragraph 6.9.1.

9.3.3.

10. PENALTIES FOR NON-CONFORMITY OF PRODUCTION

10.1. The approval granted in respect of a type of vehicle, component or separate techni-cal unit pursuant to this Regulation may be withdrawn if the requirements laid down in paragraph 6 above are not complied with or if the selected vehicles fail to pass the tests provided for in paragraph 6 above.

10.2. If a Party to the Agreement which applies this Regulation withdraws an approval it

has previously granted, it shall forthwith notify thhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmle other Contracting Parties applying this Regulation thereof by means of a communication form conforming to the model in Annexes 3A and 3B to this Regulation.

11. PRODUCTION DEFINITELY DISCONTINUED

If the holder of an approval permanently ceases to manufacture a type of vehicle or ESA approved in accordance with this Regulation, he shall so inform the authority which granted the approval, which shall in turn notify the other Parties to the 1958 Agreement which apply this Regulation, by means of a communication form conform-ing to the model in Annexes 3A and 3B to this Regulation.

12. MODIFICATION AND EXTENSION OF TYPE APPROVAL OF A VEHICLE OR ESA

12.1. Every modification of the vehicle or ESA type shall be notified to the Administrative

Department which granted approval of the vehicle type. This department may then  either:

12.1.1. consider that the modificationshttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html made are unlikely to have an appreciable adverse

effect and that in any case the vehicle or ESA still meets the requirements; or

12.1.2. require a further test report from the Technical Service responsible for conducting

the tests.

12.2. Notice of conformation of approval or of refusal of approval, accompanied by particu-lars of the modifications, shall be communicated by the procedure indicated in

paragraph 4 above to the Parties to the Agreement applying this Regulation.

12.3. The Competent Authority granting the approval extension shall assign a serial

number to the extension and so notify the other Parties to the 1958 Agreement apply-ing this Regulation by means of a communication form conforming to the models in Annexes 3A and 3B to this Regulation.

13. TRANSITIONAL PROVISIONS

13.1. As from the official date http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlof entry into force of the 03 series of amendments, no

Contracting Party applying this Regulation shall refuse to grant ECE approval under this Regulation as amended by the 03 series of amendments.

13.2. As from 12 months after the date of entry into force of this Regulation, as amended

by the 03 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type, component or separate technical unit to be approved meets the requirements of this Regulation as amended by the 03 series of amendments.

13.3. Contracting Parties applying this Regulation shall not refuse to grant extensions of

approval to the preceding series of amendments to this Regulation.

13.4. Starting 48 months after the entry into force of the 03 series of amendments to this

Regulation, Contracting Parties applying thishttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html Regulation may refuse first national registration (first entry into service) of a vehicle, component or separate technical unit which does not meet the requirements of the 03 series of amendments to this Regulation.

13.5. As from [36] months after the official date of entry into force of this Regulation, as

amended by the 04 series of amendments, Contracting Parties applying this Regula-tion shall grant approvals only if the vehicle type, to be approved meets the require-ments of this Regulation as amended by the 04 series of amendments.

13.6.

Until [36] months after the date of entry into force of the 04 series of amendments, no Contracting Parties shall refuse national or regional approval of a vehicle ap-proved to the preceding series of amendments to this Regulation.

As from [60] *), Contracting Parties may refuse first registration of a new vehhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlicle which does not meet the requirements of the 04 series of amendments to this Regu-lation.

Notwithstanding paragraphs 13.6 and 13.7 approvals of vehicle granted to the  preceding series of amendments to the Regulation, which are not affected by the 04  series of amendments, shall remain valid and Contracting Parties applying the Regu-lation shall continue to accept them.

NAMES AND ADDRESSES OF TECHNICAL SERVICES CONDUCTING APPROVAL TESTS, AND OF ADMINISTRATIVE DEPARTMENTS

The Parties to the 1958 Agreement applying this Regulation shall communicate to the United Nations Secretariat the names and addresses of the Technical Services conducting approval tests and of the Administrative Departments which grant  approvals and to which forms certifying approval or extension, refusal or withdrawal of approval, issued in other countries, are to be sent.

13.7.

13.8.

14.://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlpar

*)

ALO editorial note: text is missing, should obviously read:

“13.7 As from [60] months after the date of entry into force of the 04 series of amendments, Contracting …“

APPENDIX 1

LIST OF STANDARDS REFERRED TO IN THIS REGULATION

1.  2.

CISPR 12 "Vehicles', motorboats' and spark-ignited engine-driven devices' radio disturbance characteristics — Limits and methods of measurement", fifth edition 2001 and Amd1:2005.

CISPR 16-1-4 "Specifications for radio disturbance and immunity measuring appara-tus and methods - Part 1: Radio disturbance and immunity measuring apparatus ap-paratus *) – Antennas and test sites for radiated disturbances mesaurements" **), third edition 2010.

CISPR 25 "Limits and methods of measurement of radio disturbance characteristics for the protection of receivers used on board vehicles", second http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmledition 2002 and corrigendum 2004.

ISO 7637-1 "Road vehicles - Electrical disturbance from conduction and coupling - Part 1: Definitions and general considerations", second edition 2002 and Amd1:2008. ISO 7637-2 "Road vehicles - Electrical disturbance from conduction and coupling - Part 2: Electrical transient conduction along supply lines only on vehicles with nominal 12 V or 24 V supply voltage", second edition 2004 and Amd1:2008.

ISO-EN 17025 "General requirements for the competence of testing and calibration laboratories", second edition 2005 and Corrigendum:2006.

ISO 11451 "Road vehicles - Electrical disturbances by narrowband radiated electro-magnetic energy - Vehicle test methods":

Part 1: General and definitions (ISO 11451-1, third edition 2005 and Amd1:2008); Part 2: Off-vehicle radiation source (ISO 11451-2, third edition 2005); Part 4: Bulk current injection (BCI) (ISO 11451-4, fihttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlrst edition 1995).

ISO 11452 "Road vehicles - Electrical disturbances by narrowband radiated electro-magnetic energy - Component test methods":

Part 1: General and definitions (ISO 11452-1, third edition 2005 and Amd1:2008); Part 2: Absorber-lined chamber (ISO 11452-2, second edition 2004);

Part 3: Transverse electromagnetic mode (TEM) cell (ISO 11452-3, third edition 2001);

Part 4: Bulk current injection (BCI) (ISO 11452-4, third edition 2005 and Corrigendum 1:2009);

Part 5: Stripline (ISO 11452-5, second edition 2002).

ITU Radio Regulations, edition 2008.

IEC 61000-3-2 "Electromagnetic Compatibility (EMC) – Part 3-2 – Limits for harmonic current emissions (equipment input current ≤ 16 A per phase)", edition 3.2 – 2005  A1:2008 A2:2009.

IEC 61000-3-3 "Electromagnetic Compatibility (EMC) – Part 3-3 – Limits – Limitation of voltage changes, voltage fluctuathttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlions and flicker in public lowvoltage systems for

3.  4.  5.   6.  7.

8.

9.  10.  11.

*)**)

ALO editorial note: “apparatus“ listed twice

ALO editorial note: should obviously read “… disturbances measurements“

equipment with rated current ≤ 16 A per phase and not subjected to conditional con-nection", edition 2.0 - 2008.

12.

IEC 61000-3-11 "Electromagnetic Compatibility (EMC) – Part 3-11 – Limits – Limita-tion of voltage changes, voltage fluctuations and flicker in public low-voltage systems - Equipment with rated current ≤ 75 A per phase and subjected to conditional connection", edition 1.0 - 2000.

IEC 61000-3-12 "Electromagnetic Compatibility (EMC) – Part 3-12 – Limits for harmonic current emissions produced by equipment connected to public low-voltage systems with input current > 16 A and ≤ 75 A per phase", editionhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html 1.0 - 2004.

IEC 61000-4-4 "Electromagnetic Compatibility (EMC) – Part 4-4 – Testing and measurement techniques – Electrical fast transients/burst immunity test", edition 2.0 - 2004.

IEC 61000-4-5 "Electromagnetic Compatibility (EMC) – Part 4-5 – Testing and measurement techniques – Surge immunity test", edition 2.0 - 2005.

13.  14.  15.

16. IEC 61000-6-2 "Electromagnetic Compatibility (EMC) – Part 6-2 – Generic standards

Immunity for industrial environments", edition 2.0 - 2005.

17. IEC 61000-6-3 "Electromagnetic Compatibility (EMC) – Part 6-3 – Generic standards

Emission standard for residential, commercial and light-industrial environments",  edition 2.0 - 2006.

18. CISPR 16–2–1 "Specification for radio disturbances and immunity measuring appara-tus and methods – Part 2-1 – Methods of measurement of disturbances and immunity

://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlr– Conducted disturbances measurement", edition 2.0 – 2008.

19. CISPR 22 "Information Technology Equipment – Radio disturbances characteristics –

Limits and methods of measurement", edition 6.0 - 2008.

20. CISPR 16-1-2 "Specification for radio disturbance and immunity measuring apparatus

and methods – Part 1-2: Radio disturbance and immunity measuring apparatus –  Ancillary equipment – Conducted disturbances", edition 1.2: 2006.

VEHICLE BROADBAND REFERENCE LIMITS

Antenna-vehicle separation: 10 m

Limit E (dB?V/m) at frequency F (MHz)

30 – 75 MHz E = 32

75 – 400 MHz

E = 32   15.13 log (F/75)

400 – 1,000 MHz

E = 43

Frequency - megahertz - logarithmic

(See paragraph 6.2.2.1. of this Regulation)

VEHICLE BROADBAhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlND REFERENCE LIMITS

Antenna-vehicle separation: 3 m

Limit E (dB?V/m) at frequency F (MHz)

30 – 75 MHz E = 42

75 – 400 MHz

E = 42   15.13 log (F/75)

400 – 1,000 MHz

E = 53

Frequency - megahertz - logarithmic

(See paragraph 6.2.2.2. of this Regulation)

VEHICLE NARROWBAND REFERENCE LIMITS

Antenna-vehicle separation: 10 m

Limit E (dB?V/m) at frequency F (MHz)

30 – 75 MHz E = 22

75 – 400 MHz

E = 22   15.13 log (F/75)

400 – 1,000 MHz

E = 33

Frequency – megahertz - logarithmic

(See paragraph 6.3.2.1. of this Regulation)

VEHICLE NARROWBAND REFERENCE LIMITS

Antenna-vehicle separation: 3 m

Lhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlimit E (dB?V/m) at frequency F (MHz)

30 – 75 MHz E = 32

75 – 400 MHz

E = 32   15.13 log (F/75)

400 – 1,000 MHz

E = 43

Frequency – megahertz - logarithmic

(See paragraph 6.3.2.2. of this Regulation)

ELECTRICAL/ELECTRONIC SUB-ASSEMBLY

Broadband reference limits

Limit E (dB?V/m) at frequency F (MHz)

30 – 75 MHz

E = 62 – 25.13 log (F/30)

75 – 400 MHz

E = 52   15.13 log (F/75)

400 – 1,000 MHz

E = 63

Frequency – megahertz - logarithmic

(See paragraph 6.5.2.1. of this Regulation)

ELECTRICAL/ELECTRONIC SUB-ASSEMBLY

Narrowband reference limits

Limit E (dB?V/m) at frequency F (MHz)

30 – 75 MHz

E = 52 – 2http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html5.13 log (F/30)

75 – 400 MHz

E = 42   15.13 log (F/75)

400 – 1,000 MHz

E = 53

Frequency – megahertz - logarithmic

(See paragraph 6.6.2.1. of this Regulation)

EXAMPLES OF APPROVAL MARKS

Model A

(See paragraph 5.2. of this Regulation)

a = 6 mm min

The above approval mark affixed to a vehicle or ESA shows that the vehicle type concerned has, with regard to electromagnetic compatibility, been approved in the Netherlands (E 4) pursuant to Regulation No. 10 under approval No. 042439. The approval number indicates that the approval was granted according to the requirements of Regulation No. 10 as amen-ded by the 04 series of amendments.

Model B

(See paragraph 5.2. of this Regulation)

a = 6 mm min

://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlarThe above approval mark affixed to a vehicle or ESA shows that the vehicle type concerned has, with regard to electromagnetic compatibility, been approved in the Netherlands (E 4) pursuant to Regulations Nos. 10 and 33. *)

The approval numbers indicate that, at the date when the respective approvals were given, Regulation No. 10 included the 04 series of amendments and Regulation No. 33 was still in its original form.

*)

The second number is given merely as an example.

INFORMATION DOCUMENT

FOR TYPE APPROVAL OF A VEHICLE WITH RESPECT TO

ELECTROMAGNETIC COMPATIBILITY

The following information shall be supplied in triplicate and shall include a list of contents.

Any drawings shall be supplied in appropriate scale and in sufficient detail on size A4 or in a folder of A4 format.

Photographs, ifhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html any, shall show sufficient detail.

If the systems, components or separate technical units have electronic controls, information concerning their performance shall be supplied.

GENERAL

1. Make (trade name of manufacturer): ........................................................................

2. Type: ......................................................................................................................  3. Category of vehicle: .................................................................................................  4. Name and address of manufacturer: ........................................................................  ................................................................................................................................   Name and address of authorised representative, if any: ...........................................  5. Address(es)http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html of assembly plant(s): ............................................................................  ................................................................................................................................

GENERAL CONSTRUCTION CHARACTERISTICS OF THE VEHICLE

6. Photograph(s) and/or drawing(s) of a representative vehicle: ....................................  7. Position and arrangement of the engine: ..................................................................

POWER PLANT

8. Manufacturer: ..........................................................................................................  ................................................................................................................................  9. Manufacturer's engine code as marked on the engine: .............................................  10. Internal combushttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmltion engine:

1)

11. Working principle: positive ignition/compression ignition, four-stroke/two stroke

12. Number and arrangement of cylinders: .....................................................................

13. Fuel feed:

14. By fuel injection (compression ignition only): yes/no 1)  15. Electronic control unit:

16. Make(s): ..................................................................................................................  17. Description of the system: .......................................................................................  18. By fuel injection (positive ignition only): yes/no 1)

19. Electrical system:  20. Rated voltage: ........................................... V, positive/negative ground 1)

21. Generator:

22. Type: ...............................................................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.......................................

23. Ignition:

24. Make(s): ..................................................................................................................

25. Type(s): ..................................................................................................................

26. Working principle: ....................................................................................................

1)

27. LPG fuelling system: yes/no   28. Electronic engine management control unit for LPG fuelling:

29. Make(s): ..................................................................................................................

30. Type(s): ..................................................................................................................  31. NG fuelling system: yes/no 1)  32. Electronic engine management control http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlunit for NG fuelling:

33. Make(s): ..................................................................................................................

34. Type(s): ..................................................................................................................

35. Electric motor:  36. Type (winding, excitation): .......................................................................................

37. Operating voltage: ...................................................................................................

Gas fuelled engines (in the case of systems laid-out in a different manner, supply equivalent information)

38. Electronic control unit (ECU):

39. Make(s): ..................................................................................................................

40. Type(s): ...........................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.......................................................................

TRANSMISSION

41. Type (mechanical, hydraulic, electric, etc.): ..............................................................  42. A brief description of the electrical/electronic components (if any): ...........................

SUSPENSION

43. A brief description of the electrical/electronic components (if any): ...........................

STEERING

44. A brief description of the electrical/electronic components (if any): ...........................

BRAKES

1)

45. Anti-lock braking system: yes/no/optional   46. For vehicles with anti-lock systems, description of system operation (including any

electronic parts), electric block diagram, hydraulic or pneumatic circuit plan: ............

.................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html...............................................................................................

BODYWORK

47. Type of bodywork: ...................................................................................................  48. Materials used and methods of construction: ............................................................  49. Windscreen and other windows:  50. A brief description of the electrical/electronic components (if any) of the window

lifting mechanism: ...................................................................................................

51. Rear-view mirrors (state for each mirror): .................................................................  52. A brief description of the electronic components (if any) of the adjustment system: ...  ...........................................................................................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.....................  53. Safety belts and/or other restraint systems:  54. A brief description of the electrical/electronic components (if any): ...........................  55. Suppression of radio interference:  56. Description and drawings/photographs of the shapes and constituent materials of the

part of the body forming the engine compartment and the part of the passenger  compartment nearest to it: .......................................................................................

57. Drawings or photographs of the position of the metal components housed in the

engine compartment (e.g. heating appliances, spare wheel, air filter, steering mecha-nism, etc.): ..............................................................................................................

58. Table and drawing of radio interference control equipment: ......................................

://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlr

59.

Particulars of the nominal value of the direct current resistance and, in the case of resistive ignition cables, of their nominal resistance per metre: ................................. LIGHTING AND LIGHT SIGNALLING DEVICES

60. A brief description of electrical/electronic components other than lamps (if any): .......  ................................................................................................................................

MISCELLANEOUS

61. Devices to prevent unauthorised use of the vehicle:  62. A brief description of the electrical/electronic components (if any): ……………………..  63. Table of installation and use of RF transmitters in the vehicle(s), if applicable (see

paragraph 3.1.8. of this Regulation):

frequency bands [Hz] max. output power [W] antenna position at vehicle,

specific conditions for installa-tion and/or usehttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html

64. Vehicle equipped with 24 GHz short-range radar equipment: yes/no/optional 1).  65. Charger: on board/ external/ without 1): .........................................................................  66. Charging current: direct current/ alternating current (number of phases / frequency) 1):

................................................................................................................................

67. Maximal nominal current (in each mode if necessary):

68. Nominal charging voltage: ....................................................................................... 69. Basic vehicle interface functions: ex: L1/L2/L3/N/E/control pilot: ...............................

The applicant for type approval must also supply, where appropriate:

Appendix 1:

A list with make(s) and type(s) of all electrical and/or electronic components cohttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlncerned by this Regulation (see paragraphs 2.9. and 2.10. of this Regulation) and not previously listed.

Appendix 2:

Schematics or drawing of the general arrangement of electrical and/or electronic  components (concerned by this Regulation) and the general wiring harness arrange-ment.

1)

Strike out what does not apply.

Appendix 3:

Description of vehicle chosen to represent the type:

Body style: ................................................................................................................... Left or right hand drive: ................................................................................................ Wheelbase: .................................................................................................................

Appendix 4:

Relevant test report(s) supplied by the manufacturer from a test laboratorhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmly accredited to ISO 17025 and recognized by the Approval Authority for the purpose of drawing up the type approval certificate.

ANNEX 2B

INFORMATION DOCUMENT

FOR TYPE APPROVAL OF AN ELECTRIC/ELECTRONIC SUB-ASSEMBLY

WITH RESPECT TO ELECTROMAGNETIC COMPATIBILITY

The following information, if applicable, shall be supplied in triplicate and must include a list of contents. Any drawings shall be supplied in appropriate scale and in sufficient detail on size A4 or on a folder of A4 format. Photographs, if any, shall show sufficient detail.

If the systems, components or separate technical units have electronic controls, information concerning their performance shall be supplied.   1. Make (trade name of manufacturer): ........................................................................

2. Type: ...................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html...................................................................................................

1)

3. Means of identification of type, if marked on the component/separate technical unit:   3.1. Location of that marking: .........................................................................................  4. Name and address of manufacturer: ........................................................................  ................................................................................................................................   Name and address of authorized representative, if any: ...........................................  ................................................................................................................................  5. In the case of components and separate technical units, location and method of

affixing of the approval mark: .............http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html......................................................................

................................................................................................................................  6. Address(es) of assembly plant(s): ............................................................................

2)

7. This ESA shall be approved as a component/STU   8. Any restrictions of use and conditions for fitting: .......................................................  9. Electrical system rated voltage: ................. V, positive/negative 2) ground.

Appendix 1:

Description of the ESA chosen to represent the type (electronic block diagram and list of main component constituting the ESA (e.g. make and type of microprocessor, crystal, etc.).

Appendix 2:

Relevant test report(s) supplied by the manufacturer from a test laboratory accredited to ISO 17025 and rhttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlecognized by the Approval Authority for the purpose of drawing up the type approval certificate.

1)

If the means of identification of type contains characters not relevant to describe the component or separate

technical unit types covered by this information document, such characters shall be represented in the docu-mentation by the symbol "?" (e.g. ABC??123??). 2)

Delete where not applicable.

ANNEX 3A

COMMUNICATION

(Maximum format: A4 (210 x 297 mm))

1)

issued by: Name of administration:...................................................................................

.......................................................................................................................  ......................................................................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.................................

GRANTED concerning: 2) APPROVAL

APPROVAL EXTENDED APPROVAL REFUSED APPROVAL WITHDRAWN

PRODUCTION DEFINITELY DISCONTINUED

of a type of vehicle/component/separate technical unit 2) with regard to Regulation No. 10.

Approval number: .................................................................................................................

Extension No.: ......................................................................................................................   1. Make (trade name of manufacturer):.........................................................................  2. Type:.......................................................................................................................  3. Means of identification of type, if marked on the vehicle/component/separate techni-cal unit 2)  3.1. Location of thahttp://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlt marking:..........................................................................................  4. Category of vehicle:..................................................................................................  5. Name and address of manufacturer:.........................................................................  ................................................................................................................................  6. In the case of components and separate technical units, location and method of

affixing of the approval mark:....................................................................................

................................................................................................................................  7. Address(es) of assembly plant(s):.............................................................................  8. Additional http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.htmlinformation (where applicable): See appendix

1)

Distinguishing number of the country which issued/extended/refused/withdrew approval (see Regulation provi-sions on approval).

2)

Strike out what does not apply.

9. Technical Service responsible for carrying out the tests:...........................................  ................................................................................................................................  10. Date of test report:...................................................................................................  11. Number of test report:..............................................................................................  12. Remarks (if any): See appendix

13. Place:......................................................................................................................

14. Date:.http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html.......................................................................................................................

15. Signature:................................................................................................................  16. The index to the information package lodged with the Approval Authority, which may

be obtained on request is attached

17. Reasons for extension:.............................................................................................

Appendix to type-approval communication form No. ........ concerning the

type-approval of a vehicle under Regulation No. 10

1. Additional information:..............................................................................................  2. Electrical system rated voltage: V. pos/neg ground 2)

3. Type of bodywork:.....................................................http://www.wendangxiazai.com/b-9a18f150bb68a98270fefa3a.html...............................................  4. List of electronic systems installed in the tested vehicle(s) not limited to the items in

the information document:........................................................................................

4.1. Vehicle equipped with 24 GHz short-range radar equipment: yes/no/optional 2)  5. Laboratory accredited to ISO 17025 and recognized by the Approval Authority

responsible for carrying out the tests:.......................................................................

6. Remarks: (e.g. valid for both left-hand drive and right-hand drive vehicles):...............  ................................................................................................................................

2)

Strike out what does not apply.

文档下载网是专业的免费文档搜索与下载网站，提供行业资料，考试资料，教学课件，学术论文，技术资料，研究报告，工作范文，资格考试，word文档，专业文献，应用文书，行业论文等文档搜索与文档下载，是您文档写作和查找参考资料的必备网站。

文档下载 http://www.wendangxiazai.com/

亿万文档资料，等你来发现